## Slide 1: Building and Furniture Technology
Lesson # 01
Site Work Operations
Mr. D. Ramdeo April 2020

## Slide 2: OBJECTIVES
You should be able to:
List the factors to be considered when choosing a building site.
Discuss the advantages and disadvantages to each factor

## Slide 3: Availability of Utilities
Availability of utilities
The builder must take into account utilities such as; access roads, transportation, electrical power supply, storage security, site and staff safety, etc. in order to accumulate the estimated cost and duration of the project.

## Slide 4: Site History
2. Site history
As a builder, it is your responsibility to conduct a comprehensive investigation into the site location to determine the land history. This can be achieved by having discussions with existing land owners, researching past and present documents etc. this is mainly to determine if the land was filled or if their used to be a water course through the land etc.

## Slide 5: Soli Type
3. Soil types
The builder must determine the type of soil before construction to determine whether the soil is cohesive (clay, silty clay, sandy clay, clay loam) or non-cohesive (sand, gravel). The main purpose of determining soil types is for foundation designs.

## Slide 6: Topography
4. Topography
Topography of a building site is very important. If the site is flat, then the topography would not affect the location and layout of the structure. However, on a sloping site the topography will be a significant factor as this will affect; position of the structure, sun rise & sun set, footpaths, road access etc.
https://www.google.com/search?q=topography&oq=topography&aqs=chrome..69i57j0l7.18855j0j4&sourceid=chrome&ie=UTF-8

## Slide 7: Prospect
5. Prospect
This is determination of the views desired by the clients for the positioning of the various rooms in a building with respect to the surroundings of the building location.

## Slide 8: Aspect
6. Aspect
Aspect of a building is the arrangements of doors, windows, walls, stairways etc. to allow as much as possible natural ventilation, lighting and scenery. Prospect and aspect works together.

## Slide 9: Zoning Regulations
7. Zoning
Zoning is the process of dividing land use into four (4) categories; Residential, Industrial, Commercial and Open space use. This is achieved through the various building laws as determined by the site location. As a builder, it is important to be familiarized with the relevant building codes during the design stage of a structure.

## Slide 10: Other Factors
8. Some other factors are:
Site location
Building size
Site climate
Building cost

## Slide 11: References:
https://en.wikipedia.org/wiki/Topography
Damain Ramdeo – BFT teacher

## Slide 12: Summative Evaluation (Short answer items)
Briefly explain the difference between prospect and aspect of a building design. (4 marks)
How does site topography affect the design of a building? (5 marks)
List and briefly explain two (2) factors that would determine a foundation design. (6 marks)
State one (1) example for each of the categories in zoning. (4 marks)

## Slide 13: Summative Evaluation (Objective items; True/False)
Instruction: Indicate if the following statements are True [ T ] or False [ F ] by ticking the relevant box. (One (1) mark each)
Location and climate are factors when choosing a building site. [ T ] [ F ]
Project cost is not affected by the availability of utilities. [ T ] [ F ]
Prospect and aspect are closely related in the design process. [ T ] [ F ]
Topography determines a building location. [ T ] [ F ]
Soil type determination does not affect foundation designs. [ T ] [ F ]

## Slide 14: Short answer items - solutions
Prospect- deals with the clients desire in the positioning of the different types of rooms in the building according to the surroundings of the site. (2 mks)
Aspect- deals with the arrangements of windows, doors, walls and stairs of building to allow natural lighting, ventilation and scenery views. (2 mks)

## Slide 15: Short answer items - solution
2. Topography affects the design of a building based on whether the site is flat or sloping. If the site is flat then the overall cots will be lower, (2 mks) but if the site is sloping then the cost will be higher due to roads, walkways, foundations etc. to suit the slope (3 mks)

## Slide 16: Short answer items - solution
Any two (2) of the following;
Site history- to determine if the site was filled or any past use of the site (3 mks)
Soil types- to determine if the soil is cohesive or non-cohesive (3 mks)
Topography – sloping or flat building site will vary the foundation designs (3 mks)

## Slide 17: Short answer items - solution
One example for each of the zoning categories are; (any one of these)
Residential – apartments, townhouses, condominiums, single family homes, multi family homes.
Industrial – warehouses, factories, cold storage buildings, showroom buildings, etc.
Commercial – office buildings, retail outlets, offices, etc.
Open spaces – football fields, basket ball courts, cricket grounds, etc.

## Slide 18: Objective items - solution
T
F
T
T
F