## Slide 1: Building and Furniture Technology
Lesson # 2
Site work operations
D. Ramdeo April 2020

## Slide 2: Objectives
At the end of this lesson you should be able to:
Prepare for site work operations
List the documents the builder must acquire to start the site work operations
State the four groups of site operations
Define the terms used in site work preparation
Describe the processes used in site layout

## Slide 3: Prepare for site work operations.
When the builder is given permission to a building site, the task of preparing for and setting out the building can be commenced. These operations can be grouped under four (4) headings:
Clearing the site
Hoarding off the site
Establishment of facilities
Setting out the building

## Slide 4: Requirements
Before any of the mentioned operations can be achieved, the builder must have the following documents:
Cadastral plan
Site layout plan
Detailed building plan
Relevant building regulations and codes

## Slide 5: Clearing the site
This process may involve the:
Demolition of existing buildings
Grubbing out of bushes and trees
Removal of top soil to reduce levels
Addition of soil to increase levels
The method chosen for site clearance work will be determined by:
the scale of development
consideration for the environment
any adjacent buildings.

## Slide 6: Hoarding off the site
Hoarding is the process of erecting fences or barriers in the perimeter of the building site. Its general purpose is to:
Provide protection to the public
Secure plants (tools & equipment) and materials
General security of work site
Reduction of interference and interruptions

## Slide 7: Hoarding: Types
Two forms of hoard commonly used in site preparation:
Vertical hoarding
consists of a series of close-boarded panels securely fixed to resist wind; theft and accident impact loads.
Fan hoardings
mainly designed and installed to provide protection from falling objects.
It is placed at a level above the normal traffic height and arranged in such a manner that any falling debris is directed back towards the building site.

## Slide 8: Vertical Hoarding

## Slide 9: Fan Hoarding

## Slide 10: Establishment of facilities
The establishment of facilities is considered as the most important operation in the preparation of site work. Some of the main categories are:
Site offices
Sanitary facilities
Equipment and material storage
Water
Electricity

## Slide 11: Setting out the building: Task 1
The first task is to establish a base line from which the building can be set out.
This is shown in Figure 1 on the next slide

## Slide 12: Setting out the building: Task 1
Figure 1 footpath / roadway to establish baseline

## Slide 13: Setting out the building: Task 2
After the baseline has been established, the main setting out lines can be set using corner profiles as shown in Figure 2
Go to Figure 2 on the next slide

## Slide 14: Setting out the building: Task 2

## Slide 15: Setting out the building
Corner profiles can be either continuous or stopped.
After setting out the main building lines (setting out lines) as shown in Fig 2, the 3:4:5 method of checking is performed to ensure the corners are right angles
This can also be done by measuring the diagonals.
Trench and wall widths are then marked for layout on the batter boards as shown in Fig 2

## Slide 16: References
  Mr Damian Ramdeo – BFT Teacher
Photos::
Wikimedia commons

## Slide 17: Summative evaluation Objective items
Which of the following plans a builder will use to set out the main building lines?
(A) Cadastral (B) Site (C) Building (D) Building detail
2. The term “earthing” can be referred to as…
(A) cutting of trees (B) demolishing old buildings
(C) removal or addition of soil (D) stripping the site
Which operation is performed first in the preparation of site work operation?
(A) Addition of soil to level site (B) Removal of soil to level site
(C) Hoarding off the site (D) Grubbing out bushes and trees

## Slide 18: Summative evaluation Objective items
Why is salvaging important when demolishing old buildings on a site?
(A) For recycling purposes ( B) To save the materials to burn
(C) To distribute the materials amongst the workers
(D) To be used for scaffolding
5. What does “stripping the site” refers to in site preparation?
(A) Protection of the public (B) Disposing of old debris
(C) Cutting of trees and bushes (D) Reduction of building interruptions
Hoarding off a building site is the process of….
(A) laying out a building (B) removal of top soil
(C) storage of materials (D) securing a building site

## Slide 19: Summative evaluation – cont’d
5. Site offices are sometimes used to conduct “tool box meetings” for the general purpose of….
(A) roll call of the workers (B) discussion of the progress of work
(C) plan activities for after work (D) discuss workers salaries
Which of the following can be used to verify square of a building layout?
(A) Measuring the perimeter (B) Using the 3:4:5 method
(C) Leveling the site boundary line (D) Measuring the building base line

## Slide 20: Answer sheet
B
C
D
A
C
D
B
B