## Slide 1: Caribbean Vocational Qualification
Regional Occupational Standard (ROS)
Motor Vehicle Engine Systems

## Slide 2: Motor Vehicle Engine Systems
Unit: ASREMS0021A
Service engines and associated engine components
Changing the engine oil in a vehicle

## Slide 3: How to change the engine oil in a vehicle
https://www.youtube.com/watch?v=ms9Pli_2gOc
Click on the link and look at the video on changing engine oil.
Take note of the steps carefully!!!
Review the information in the following slides
Attempt the Worksheet.

## Slide 4: Materials
Materials Required:
Oil
Oil filter
Replacement drain plug washer (depending on application)

## Slide 5: Safety procedures to follow
Check the car manual to locate where jacks and jack stands are to be placed
Use an oil tray large enough to collect the old oil so that it does not spill all over the floor
Place the oil tray under the drain hole and position it so that the oil doesn’t get all over the floor
Always use jack stands
If oil spills, clean it up immediately
Get the manufacturer’s torque for tightening the drain plug
Always use a funnel for pouring oil to avoid spills
Get rid of the old oil responsibly

## Slide 6: Tools & equipment
Tools Required:
Wrench to remove drain plug (box end or socket)
Oil filter wrench
Oil drain pan
Funnel
Latex gloves
Jack and jack stands or ramps (optional, depends on ground clearance

## Slide 7: How to change the vehicle engine oil
Click on the links below and look at the process of changing a vehicle engine oil:
https://www.wikihow.life/Change-the-Oil-in-Your-Car
Now, review the information given on the following slides.

## Slide 8: Steps to follow
Check the type and amount of oil needed.
Get together your filter, wrenches, and other supplies.
Make sure you warm up the engine first.
Prepare your vehicle – jack up the car safely
Locate the oil filter and drain plug.
Drain the oil.

## Slide 9: Steps to follow
Tighten the drain plug.
Change the oil filter.
Place some oil around the seal of the new filter to lubricate it before replacing the filter

## Slide 10: Completing the engine oil change
To complete the process:
Take down the car so that it is level
Pour in the new oil leaving about a litre
Check the oil level
Add more oil if required.
Start the car engine to allow the oil to move around the engine.
Recheck oil level to ensure adequate oil is in the engine.

## Slide 11: Self Assessment
Go to the self assessment activity and follow the instructions
Upon completion, check yourr esponses to those on the answer sheet.
How did you do??

## Slide 12: references
Online:
- Wikimedia commons