## Slide 1: Caribbean vocational qualification
Motor Vehicle Engine System Level 1

## Slide 2: Objective
ASREMS0011A
Prepare for general servicing/repairing of motor vehicle
Doing a service check on vehicles

## Slide 3: Preventative maintenance
Preventative vehicle maintenance ensures your vehicle achieves optimal fuel mileage.
Neglecting to change basic engine parts like oils and filters can reduce fuel mileage and increase wear and tear.

## Slide 4: Preventative maintenance: Types of Car Service
An interim/basic service is a less extensive service that checks over the main parts of your car, and it should be carried out every 6 months or every 10,000 kilometers.
A full service is a complete check of the whole car, which should be carried out annually or every 20,000 kilometers.

## Slide 5: What is a full vehicle service??
Car servicing is actually an set of maintenance procedures carried out in frequent intervals to support for smooth riding of your car.

## Slide 6: A basic vehicle engine service
A basic service will typically include an oil and filter change; a visual inspection of all the key fluids in the engine; as well as a check of other key components which ensures the vehicle is in the best possible condition for optimal mileage.

## Slide 7: A basic vehicle engine service
These routine checks ensures that we have no surprises between services or flags warning conditions.

## Slide 8: Pre-service checks
Pre-service checks are a part of preventative maintenance for vehicles which is a visual inspection to determine whether parts or the vehicle is in a road worthy condition.
A preventative maintenance program allows for the vehicle to be inspected on a routine basis (specific time period) so that any items that are at or approaching a cut-off point can be corrected.
Preventative maintenance is composed of standardised inspections and maintenance
It allows for longegivity of the vehicle at a good operational level

## Slide 9: Checks can be grouped
Pre-engine check
Under bonnet
Under the car (vehicle raised)
Vehicle lowered (tires)
Finish
A check list can be created for each stage

## Slide 10: Pre-engine check
What is included:
Check car history
Check timing belt replacement interval
Check for damage to bodywork, lamps and trims
Check condition of all seat belts
Check operation of interior and exterior lights
Check operation of ABS and/or air bag warning lights.

## Slide 11: Pre-engine check
Check windscreen washers and wipers.
Check horn.
Check cabin filter
Lubricate all door hinges, locks, and bonnet catches.
Check fuel

## Slide 12: Under the bonnet - fluids
Check the level of all Fluids:
Engine oil
Radiator coolant
Brake fluid
Power steering fluid
Windscreen washer fluid
Clutch fluid (manual cars)
Gearbox oil
Differential fluid

## Slide 13: Fluid levels
There are markers showing minimum and maximum levels
Make sure the fluids are at the recommended full level
Note fluids that are below the minimum levels
Top up fluids to appropriate levels

## Slide 14: Under the bonnet – belts & hoses
Radiator hoses – check for leaks and cracking
Engine air filter – check that it is clean
Battery – look for corrosion around terminals; clean & lubricate
Drive belts – ensure none are loose or squeaking on start-up
Unusual engine noises – hard to start, ticking, hissing or clunking

## Slide 15: Under car – vehicle raised
Visual Check:
Oil filter and sump plug for leaks or wear
Fuel lines for leaks
Condition of the exhaust pipes
Brake pads and rotor discs
Tire wear

## Slide 16: Tire check
Check tire lug nuts
Air in tires
Check air in spare tire
Check the emission from the exhaust

## Slide 17: References
Youtube how to
Wikipedia how to
Wikimedia commons for photos